Elektronica-ICT / Elektronische systemen 2

Sound measurement with integration of Arduino Pedalshield
Authors	Michiel Parthoens / Loïc Schillings

Content

# Introduction
This application note delves into the innovative fusion of sensors with the Arduino Pedalshield. The utilization of sensors for capturing sounds and vibrations, coupled with the signal-enhancing capabilities of the Pedalshield, provides us with new possibilities for real-time monitoring and analysis.

In this document, we explore the integration between sensor data acquisition and signal processing using the Arduino platform. Specifically, throughout this project, we aim to achieve three primary goals: the effective utilization of a sensor dedicated to capturing sound, the proper utilization of the Pedalshield for signal amplification and manipulation, and finally, the display of the enhanced and possibly modified signal on an OLED screen using the Arduino Due
# Hardware and software
Before we can discuss the project we need to explain the used hardware and software. This section contains the hardware and software used in the project and the research done to achieve the end result.
## Hardware
A variety of hardware components were used in this project. An Arduino Due was crucial for signal interpretation. The Pedalshield posed the greatest challenge; it connects to the pins of the Arduino Due and amplifies the signals from the sensors. Various sensors were tested and employed as input for the Pedalshield, enhancing its functionality. Additionally, a range of hardware plugs and cables were utilized to establish the required electrical connections,
### Research
Before commencing the project, thorough research was imperative. Initially, attention was directed towards the Arduino Due, followed by a comprehensive examination of the Pedalshield. Subsequently, the sensors were looked at. Finally, research was conducted to identify any additional required hardware components.
The research conducted for the Arduino Due was relatively brief. The primary focus was understanding the pin layout of the Arduino. Additionally, we delved into discovering the parameters of the ADC and DAC pins. These pins are responsible for receiving signals from the Pedalshield as well as transmitting any modified signals.

After the pinout and the functions of these pins from the Arduino due were known, the pedalshield was looked at. Firstly we needed to know what the pedalshield does and how it worked. To achieve this, the electrical schematics were used.

In the schematics it is obvious that the pedalshield electronics are divided into four main parts. These parts being: “The input stage, The output stage, The power supply and The user interface”. The purpose of the power supply is obvious.
The user interface is a series of switches and potentiometers connected to io pins on the Arduino. There is also a large button i.e. “the pedal”. the provided hardware in the user interface can be customized in the Arduino code.

The input stage takes the incoming signal and amplifies it. It also makes sure that the signal is converted to a positive voltage. This is necessary because the Arduino due’s ADC pins cannot measure a negative voltage. After converting the voltage the modified signal goes to the Arduino where it can be altered. The altered signal then goes to the output stage which does exactly the opposite of the input stage.
### Sensors

Sound sensors play a crucial role across various fields, from healthcare to consumer electronics. Offering the capability to detect and measure sound waves in different environments. In this section, three distinct sound sensors are explored : the Agilent Technologies Stethos, the Korg CM-200 contact sensor, and the Keyes KY-038 sound detector module. Each sensor brings unique features and functionalities suited for a wide array of applications.

#### Agilent Technologies Stethos

The Agilent Technologies Stethos is a sound sensor specifically made for medical applications, particularly in cardiology and respiratory applications. the Stethos has high sensitivity and accuracy in capturing subtle physiological sounds such as heartbeats, breath sounds, and murmurs. Its compact design makes it an indispensable tool in clinical settings where precise and reliable sound detection is essential.

Key Features:

Exceptional sensitivity for detecting faint physiological sounds.
Wide frequency range tailored for cardiological and respiratory assessments.
Seamless integration with standard medical equipment for streamlined workflows.

#### Korg CM-200 Contact Sensor

The Korg CM-200 contact sensor represents a sound detection solution primarily designed for music applications. Utilizing contact transduction, this sensor captures vibrations directly from instrument surfaces. This means there is an accurate and reliable sound detection even in noisy environments. Whether for tuning instruments or recording performances, the CM-200 offers musicians and audio engineers a precise tool for capturing and analyzing sound.

Key Features:

Contact-based transduction for enhanced noise immunity and signal precision.
Durable construction suitable for rigorous music performance environments.
Compact and lightweight design for seamless integration with musical instruments and recording equipment.

#### Keyes KY-038 Sound Detector Module

The Keyes KY-038 sound detector module serves as an accessible and cost-effective solution for hobbyists, students, and enthusiasts interested in sound-based projects. This module detects sound pressure variations and outputs corresponding electrical signals, making it compatible with a wide range of microcontrollers and development platforms. The KY-038 module is an excellent choice for educational experiments, DIY projects, and prototyping.

Key Features:

User-friendly module suitable for beginners and hobbyists.
Analog output for seamless integration with microcontrollers and development boards.
Adjustable sensitivity for adapting to diverse sound environments and project requirements.

In summary, the Agilent Technologies Stethos, Korg CM-200 contact sensor, and Keyes KY-038 sound detector module offer distinct advantages made for specific applications and user needs. Whether in medical diagnostics, music performance, or educational experimentation, these sound sensors empower users with the capability to capture, analyze, and utilize sound data effectively.
### Additional hardware

## Software

# Results
# User Experience
# Discussion
# Conclusion
# Reference list
# Attachment